## Slide 1: Visualize and Analyze Energy Data
Mauricio Carvajal

## Slide 2: Agenda
Visualizations with Analysis
Time Series Visualizations with Analysis
Linear Regression Forecast Visualizations with Analysis
Decomposition Visualizations with Analysis
Holt Winters Forecasting and Analysis
Correlations or predictions
Summary statement that addresses the goal of this project. Has the goal been met
Business recommendations
Lessons learned

## Slide 3: Visualizations with Analysis

## Slide 4: day visualization
Learnings:
  Submeter1: Used in the kitchen, is active mostly in food time
  Submeter2: Laundry Room, most of the cycles are related to the tumble-drier.
  Submeter3: Water Heater &AC, used on before/after work times, morning probably used AC.

## Slide 5: Week visualization
Learnings:
  Submeter1: Peaks mostly on the weekends due to more time cooking
  Submeter2: 2 Peaks, probably 2 times do the laundry.
  Subtemer3:
    Water Heater &AC has a parent usage true the week.

## Slide 6: Month visualization
Learnings:
  Submeter1: present a peak behavior, submeter 2 same, and the case of water heater and AC preset a pattern

## Slide 7: day visualization
Learnings:
  The overall power consumption is 2/3 by the submete3.
  Submeter 1 and 2 present similar power consumption.
  A plan to reduce consumption is to lower the use submeter3

## Slide 8: Time Series Visualizations with Analysis

## Slide 9: Weekly power consumption of Submeter 3
Details:
  Submeter3: Water header & AC
  Subset: 1 observation per week on Mondays at 8:00pm for 2007, 2008 and 2009
  Has some zeros, due to is a sutset and we are taking 1 specify time.

## Slide 10: Monthly power consumption 2007-2009
Details:
  Submeter2: Laundry Room
  Frequency:12
  1 observation per month on day 2 at 7:05am
Details:
  Submeter2:Laundry Room
  Frequency: 12
  Average power consumption per month
  This was taking to avoid zeros

## Slide 11: Quarterly power consumption 2007-2009
Details
  SubMeter1: Kitchen
  Sample: 1 observation per quarterly,
    It’s the average of all the quarterly power consumption
  Frequency: 4 per year

## Slide 12: Linear Regression Forecast Visualizations with Analysis

## Slide 13: Weekly Forecasts using linear regression
Details:
  Weekly Forecasts using linear regression
  SubMeter 3: Water Hearter &AC
  Time period:2007-2009
  Frecuency:52
  Confidence levels: 80-90

## Slide 14: Average Monthly Forecasts using linear regression
Details:
  SubMeter 2: Laundry Room
  Time period:2007-2009
  Observations: Average power consumption per month
  Frecuency:12
  Confidence levels: 80-90

## Slide 15: Average Quarterly Forecasts using linear regression
Details:
  Submeter 1: Kitchen
  Time period:2007-2009
  Observations: Average power consumption per quarterly
  Frecuency:4
  Confidence levels: 80-90

## Slide 16: Comparison chart
Model | Residual Stander Error | Multiple R2 | Adjusted R-Squared | F-statistic | Pvalue
SubMeter1_QuarterlyModel | 0.1373 on 7 degrees of freedom | 0.7566 | 0.6175 | 5.439 on 4 and 7 DF | 0.02596
SubMeter2_MonthlyModel | 0.2735 on 23 degrees of freedom | 0.6605 | 0.4834 | 3.729 on 12 and 23 DF | 0.00327
SubMeter3_WeeklyModel | 6.871 on 104 degrees of freedom | 0.3831 | 0.07461 | 1.242 on 52 and 104 DF | 0.1747
The QuaterlyModel and MonthlyModel have R2 ~.7 that interpretect the relationship between the output vs input, or the goodness of-fit
The QuaterlyModel and MonthlyModel have p value close to zero, means that we can rejet the null hypothesis, which is signal of good models

## Slide 17: Decomposition Visualizations with Analysis

## Slide 18: Decomposing a Seasonal Time Series
Details:
  Weekly Forecasts using linear regression
  SubMeter 3: Water Hearter &AC
  Time period:2007-2009
  Frecuency:52

## Slide 19: Decomposing a Seasonal Time Series
Details:
  SubMeter 2: Laundry Room
  Time period:2007-2009
  Observations: Average power consumption per month
  Frecuency:12

## Slide 20: Decomposing a Seasonal Time Series
Details:
  Submeter 1: Kitchen
  Time period:2007-2009
  Observations: Average power consumption per quarterly
  Frecuency:4

## Slide 21: Comparison chart
 | SubMeter 1 |  |  | SubMeter 2 |  |  | SubMeter 3 |  | 
 | Seasonal | Trend | Random | Seasonal | Trend | Random | Seasonal | Trend | Random
Min. | -0.28847 | 1.088 | -0.14205 | -0.61035 | 1.098 | -0.340531 | -3.70143 | 1.865 | -10.5726
1st Qu. | -0.05038 | 1.119 | -0.08485 | -0.02773 | 1.129 | -0.147322 | -3.11008 | 2.481 | -1.5341
Median | 0.03340 | 1.132 | -0.00589 | 0.02112 | 1.285 | -0.006557 | -2.81201 | 3.058 | -0.1784
Mean | 0.00000 | 1.151 | -0.00589 | 0.00000 | 1.332 | -0.006557 | 0.09312 | 3.329 | -0.2217
3rd Qu. | 0.08378 | 1.187 | 0.07307 | 0.15616 | 1.544 | 0.134209 | 5.50530 | 3.817 | 1.0909
Max. | 0.22168 | 1.231 | 0.13026 | 0.32186 | 1.616 | 0.327418 | 14.62068 | 6.663 | 10.1293

## Slide 22: Holt Winters Forecasting and Analysis

## Slide 23: HoltWinters Forecast weekly power consumption
  Weekly Forecasts using Holtwinters
  SubMeter 3: Water Hearter &AC
  Time period:2007-2009
  Frecuency:52

## Slide 24: HoltWinters Forecast Monthly power consumption
  SubMeter 2: Laundry Room
  Time period:2007-2009
  Observations: Average power consumption per month
  Frecuency:12

## Slide 25: HoltWinters Forecast quarterly power consumption
  Submeter 1: Kitchen
  Time period:2007-2009
  Observations: Average power consumption per quarterly
  Frecuency:4

## Slide 26: Suggestion Improving analysis

## Slide 27: Suggestion Improving analysis
Besides we have a lot data, ~2 millions of observations, for time series, it only represent 3 seasons 2007, 2008, 2009. So will be need to have more information and not that level of granularity.
More than the 50% of the total of power consumption, is not measure by sub_meter1,2,3. For better analysis will be needed to identify the top power consumptions items in a house and add the sub_meter.

## Slide 28: Summary Statement

## Slide 29: Summary Statement
Go with deeper analysis of the household data, using visualization and predictive models in order to get insights that help the home owners to make more informed decisions bout the power consumption.

## Slide 30: business recommendations

## Slide 31: business recommendations
The top power consumption of the 3 sub meters is the submeter 3.
  This contains the water head and AC
  For power reduction can be focus on this submeter
Overall most power consumption is not measure by any sub-meter,
  This can be reviewing using the formula that provide the data =.(global_active_power*1000/60 - sub_metering_1 - sub_metering_2 - sub_metering_3)
  Additional sub-meter can be beneficial for more accurate for better analysis and control of the power.
Predictions models can be using for forecasting the power consumption.
  For example using the hotwinters

## Slide 32: business recommendations
Distribution of the power consumption.
  Looking the distribution and the time owner can understand where are the peaks moments and avoid them
There overall trend of the power consumption going lower for submeter2.
  People are more concern on the environmental issues, and reducing the consumption the laundry room.

## Slide 33: lessons learned

## Slide 34: lessons learned
Sample large data sets can be beneficial time reductions analysis.
For time series, the observations monthly or quarterly need to gather the average power consumption, due to it has a lot zeros that are not representing.
R square R square adjusted and p-value provide a overview of the goodness of the predictions models.
Time series can be decomposition in trend, seasonal, random components.
Deleting the seasonal component help to create a accurate predative models
Hot-winter forecasting help to create a model for predictive.